## Slide 1
EX3030/EM4012 Heat, Mass and Momentum Transfer Transient Heat Transfer 1
1
Originally by Dr Mark Stewart
Presented by Dr M. Bannerman
Notes: 1

## Slide 2
Course Materials
2
EX3030/EM40JN
Pre-recorded Lectures
Lecture Notes
Tutorial sheet
Tutorial Solutions
Class recordings (review of lecture notes + worked examples)
Notes: 2

## Slide 3
Weekly Tests
3
EX3030/EM40JN
Week 7 Test Details:
“This test is on Transient Heat Transfer which we have covered during week 7 of the course. There will be a total of 7 multiple choice questions . Four of the questions will be descriptive based (worth 10 points each) and 3 will involve some calculations (worth 20 points each). Topics include general transient heat transfer, the lumped capacitance method, analytical methods and numerical methods.
Note: This test will auto-submit at the end of the exam time.”
The weekly tests continue…
Notes: 3

## Slide 4
Transient Heat Transfer
4
So far, we have only considered steady state problems i.e., when there is no dependency on time and
However, many situations in practice will involve transient (or unsteady) effects, where
For example, any heating or cooling process involving solids or liquids
Typically, these types of problems are more complicated to solve than their steady-state counterpart
This week we will learn more about methods we can use to solve problems in transient heat transfer
Introduction
EX3030/EM40JN
Notes: 4

## Slide 5
Transient Heat Transfer
5
Methods of Analysis
EX3030/EM40JN
Lumped System Analysis (or Lumped Capacitance Method)
Temperature is a function of time only
Analytical Methods
Temperature is a function of time and one space coordinate
Numerical Methods
Temperature is a function of time and all three space coordinates
Increasing complexity
Increasing generality
Notes: 5

## Slide 6
Transient Heat Transfer
6
Methods of Analysis
EX3030/EM40JN
Lumped System Analysis (or Lumped Capacitance Method)
Temperature is a function of time only
Analytical Methods
Temperature is a function of time and one space coordinate
Numerical Methods
Temperature is a function of time and all three space coordinates
Increasing complexity
Increasing generality
Notes: 6

## Slide 7
Lumped System Analysis
7
Some objects behave like ‘lumps’ when subjected to a heat transfer process and their internal temperature remains approximately uniform throughout
We call the method to analyse these types of objects Lumped System Analysis or sometimes the Lumped Capacitance Method
The simplest type of unsteady heat transfer problem, T(t)
Applicable in many situations e.g. heating/cooling of simple geometrical objects
Useful for estimating e.g. time it will take a given body to reach a certain temperature or for a given time, we can determine the temperature
Introduction
EX3030/EM40JN
Notes: 7

## Slide 8
Assumptions Behind LSA
8
Distribution of temperature is spatially uniform
Main assumption behind Lumped System Analysis:
EX3030/EM40JN
Example of a body with a spatially-uniform temperature distribution at time t (left) and some time later at t+Δt (right). Temperature changes are seen to happen equally at all points throughout the body
Notes: 8

## Slide 9
Thermal Energy Balance
9
Consider a sphere of mass and surface area cooling outside of a furnace. Assume the ball is homogenous, with constant heat capacity , constant thermal conductivity and uniform temperature distribution
A thermal energy balance shows:
and noting that and gives:
Example with a sphere
EX3030/EM40JN
Schematic of a steel sphere cooling outside of a furnace in an environment with constant temperature and heat transfer coefficient
Notes: 9

## Slide 10
Governing Equation
10
Continuing from previous slide, we set up our integration from = 0, when to time at which :
And after performing the integration we get:
Taking the exponential of both sides and rearranging leaves us with the desired result:
where
Example with a sphere (cotd)
EX3030/EM40JN
Notes: 10

## Slide 11
Estimating Heat Transfer
11
Once we get the temperature from the governing equation that we just derived, it becomes possible to estimate the convection heat transfer rate between the body and its environment
Likewise, the total amount of heat transfer between and is simply:
And the maximum heat transfer between the body and its surroundings is:
Example with a sphere (cotd)
EX3030/EM40JN
Notes: 11

## Slide 12
The Time Constant Term
12
Example of the effect of the time constant b on the cooling rate of an object in a ‘lumped system’. The values chosen in the example are for illustrative purposes only
EX3030/EM40JN
Rearranging the general equation in terms of temperature :
and plotting the results for selected values of the time constant term :
Notes: 12

## Slide 13
General Observations
13
General observations on the Lumped Capacitance Method
Temperature of the body approaches the surrounding temperature exponentially
Larger values of the time constant term indicate higher rate of temperature decay (rise)
Bodies with larger mass take longer to heat/cool, particularly if they also have large heat capacity
EX3030/EM40JN
Notes: 13

## Slide 14
A (very practical) Example
14
Based on what we’ve just seen let’s try to put it in practice by attempting to answer an important question:
How long does it take to boil an egg?
Use the lumped capacitance method…
Do the results make sense?
See also “How long does it take to boil an egg? A simple approach to the energy transfer equation” (Roura et al., 2000) for an alternative scientific approach to the problem
Boiling an egg
EX3030/EM40JN
Notes: 14

## Slide 15
The Actual Way to Boil an Egg
15
Advice from Heston
EX3030/EM40JN
Extract from the Guardian: https://www.theguardian.com/lifeandstyle/2014/nov/11/how-to-boil-an-egg-the-heston-blumenthal-way
After relentless trials, here is my formula for the perfect boiled egg:
Step 1. Take a small saucepan with a glass lid and carefully place a single egg (or two, or three) inside it. Burford brown eggs have a nice orange yolk. Fill the pan so the water only just covers the eggs – not even a millimetre more. If you had a centimetre of water covering the egg then you could still get the same result, but you’d have to play with the timing.
Step 2. Put the pan on maximum heat with the lid on and bring to the boil.
Step 3. As soon as the water starts to bubble, remove from the heat. As you take the pan off, set a timer for six minutes; keep the lid on. Make sure you time it exactly, and you’ll end up with the perfect egg.
Notes: 15

## Slide 16
Biot Number
16
Assumption of a lumped system not always the most appropriate
Define the dimensionless Biot Number, Bi:
where is the characteristic length, is the volume of the body and is the surface area for convection
Approach is valid when Bi < 0.1
When is the approach valid?
EX3030/EM40JN
Notes: 16

## Slide 17
Worked Example 1
17
Thermo-couple junction
EX3030/EM40JN
A temperature sensing element (thermo-couple junction) is placed in a gas stream. Assume the sensor is perfectly spherical.
The sensor's thermo-physical properties are:
Thermal conductivity, = 20 [W/m·K]
Specific heat capacity, = 400 [J/kg·K]
Density, = 8,500 [kg/m3]
The convection coefficient between the sensor surface and the gas is ℎ = 400 [W/m2·K]
Determine the sensor diameter needed for the thermo-couple to have a time constant of 1 second.
If the sensor is at 25°C and is placed in a gas stream that is at 200°C, how long will it take for the centre of the sensor to reach 199°C?
Notes: 17

## Slide 18
Summary
18
“Do not dismiss lumped-capacity analysis because of its simplicity. Because of uncertainties in the convection coefficient, it may not be necessary to use more elaborate analysis techniques.” (Holman, 2010, p143)
EX3030/EM40JN
The simplest type of unsteady heat transfer problem, T(t)
Applicable in many situations e.g. heating/cooling of simple geometrical objects
Useful for estimating e.g. time it will take a given body to reach a certain temperature or for a given time, we can determine the temperature
Strictly speaking, Bi < 0.1 to obtain acceptable results so always check Bi first
Summary of the lumped capacitance method
Notes: 18

## Slide 19
Thanks for your attention
19
EX3030/EM40JN
Notes: 19