## Slide 1
EX3030/EM4012 Heat, Mass and Momentum Transfer Transient Heat Transfer 2
1
Originally by Dr Mark Stewart
Presented by Dr M. Bannerman
Notes: 1

## Slide 2
Recap
2
Small objects with high thermal conductivity can often be modelled as ‘lumps’ with a single, uniform temperature that varies only with time,
Governing equation of LCM:
The validity of the approach needs to be checked for a given problem:
Approach is valid when Bi < 0.1
Lumped Capacitance Method (LCM)
EX3030/EM40JN
Notes: 2

## Slide 3
Transient Heat Transfer
3
Methods of Analysis
EX3030/EM40JN
Lumped System Analysis (or Lumped Capacitance Method)
Temperature is a function of time only
Analytical Methods
Temperature is a function of time and one space coordinate
Numerical Methods
Temperature is a function of time and all three space coordinates
Increasing complexity
Increasing generality
Notes: 3

## Slide 4
Analytical Methods
4
For Biot number > 0.1, we can no longer assume and we need an alternative approach to accurately model transient heat transfer processes for
Analytical methods can be applied to solve the simplest of these cases, i.e., when
There are three commonly encountered geometries where we can make this assumption
Introduction
EX3030/EM40JN
Plane Wall Long Cylinder Sphere
Notes: 4

## Slide 5
Heat Equation
5
Heat equation for 1-D geometry i.e. :
with initial conditions:
and boundary conditions:
After non-dimensionalising the heat equation becomes:
and initial and boundary conditions become:
We first simplify and non-dimensionalise the heat equation:
EX3030/EM40JN
Notes: 5

## Slide 6
Dimensionless Variables
6
Dimensionless temperature
Dimensionless spatial coordinate
Dimensionless heat transfer coefficient (Biot Number)
Dimensionless time (Fourier Number)
There are 4 dimensionless variables
EX3030/EM40JN
Notes: 6

## Slide 7
Solution Methods
7
One-term approximation and look-up tables
Temperature charts of Heisler and Gröber
These approaches are only strictly valid when Fourier Number
There are two approaches to the solution of analytical heat transfer problems
EX3030/EM40JN
Notes: 7

## Slide 8
Temperature Changes
8
Plane wall
Cylinder
Sphere
At the centreline
Approach 1: One term approximations
EX3030/EM40JN
is zeroth order Bessel function of 1st kind
and are coefficients, dependent only on the Bi number
Expression for is the same for all three geometries
Notes: 8

## Slide 9
Temperature Changes
9
The values of , and have been tabulated for ease of reference:
Approach 1: Look up tables
EX3030/EM40JN
Note, interpolation is usually required to get the required values
Notes: 9

## Slide 10
Temperature Changes
10
Approach 2: Heisler charts
EX3030/EM40JN
Chart 1: for determining the centreline temperature at any given time
Chart 2: get the temperature at any given location and time
Note, showing examples for plate/plane wall geometry – similar charts available for sphere and cylinder geometries too
Notes: 10

## Slide 11
Worked Eggample 1
11
The scenario (from Cengel, 2002, p224):
An ordinary egg can be approximated as a 5 cm diameter sphere. The egg is initially at a uniform temperature of 5°C and is dropped into boiling water at 95°C. Taking the convection heat transfer coefficient to be h = 1200 W/m2·°C, determine how long it will take for the centre of the egg to reach 70°C.
Let’s try again to figure out how long to boil our egg…
EX3030/EM40JN
Notes: 11

## Slide 12
Estimating Heat Transfer
12
In addition to temperature, we can also make some estimations of maximum and actual heat transfer
Approach 1: One term approximations
EX3030/EM40JN
Plane wall
Cylinder
Sphere
is zeroth order Bessel function of 1st kind
and are coefficients, dependent only on the Bi number
Notes: 12

## Slide 13
Estimating Heat Transfer
13
Approach 2: Gröber charts
EX3030/EM40JN
Notes: 13

## Slide 14
Worked Example 2
14
A hot dog, initially at a uniform temperature of 20°C, is dropped into a pan of boiling water, which is at a temperature of 94°C. The convection heat transfer coefficient between the hot dog and the water is ℎ = 467 W/m2℃
EX3030/EM40JN
The hot dog is 12.5 cm long and 2.2 cm in diameter with the following properties:
Specific heat capacity, = 3,900 J/kg·°C
Density, = 980 kg/m3
Thermal conductivity, = 0.771 W/m·°C
Determine the centre and the surface temperatures of the hot dog 4 minutes after the start of cooking
Determine the amount of heat transferred to the hot dog
Notes: 14

## Slide 15
Background Assumptions
15
EX3030/EM40JN
The following are some conditions for using the Heisler and Gröber charts that you should be aware of:
the body is initially at a uniform temperature;
the temperature of the surroundings is constant and uniform;
the convective heat transfer coefficient is constant and uniform and;
there is no heat generation in the body.
There are some limiting assumptions inherent in the analytical approach
Notes: 15

## Slide 16
Summary
16
EX3030/EM40JN
Applicable to simplified one-dimensional geometries: plane wall, cylinder and sphere
Two approaches to solve the problems: (1) 1-term approximation and look up tables or (2) Heisler and Gröber charts
Choice of equation and chart depends on the geometry of the problem
Can use the technique to understand temperature distribution at different locations within the body at different times and calculate corresponding heat transfer
Valid for situations where Fourier number
Summary of the Analytical Methods
Notes: 16

## Slide 17
Thanks for your attention
17
EX3030/EM40JN
Notes: 17